## Slide 1: 10320 CS410001 Computer Architecture
Project #1 Tutorial
First submission date: 4/4
Second submission date: 4/11

## Slide 2
Project #1 Overview
Development Environment
Demonstration

## Slide 3: Project #1 Overview

## Slide 4: Objective
Design a single-cycle, functional processor simulator based on MIPS ISA
  More details in Appendix A
Design your own test case

## Slide 5: Single Cycle Processor Simulator
Simulator
MIPS Processor
Register File
Data Memory
Instruction Memory
Read/Write
Read (Fetch)
dimage
(binary file)
iimage
(binary file)
Simulation steps:
  (1) Fetch Instruction → (2) Decoding → (3) Execution(translation/emulation)
Fetch Instruction:
  Big-endian / Little-endian (memory/register )
Decoding
  R-type
  I-type
  J-type

## Slide 6
Big-endian format
Register 0 is constant 0.
Both memory sizes are 1K bytes.
Execution terminates after “halt”.
An error handler is needed.
  More details in Appendix D
Name the exe file as single_cycle, and no more cmd-line arguments.
Input files and output files are in the same directory.

## Slide 7: MIPS Register Conventions

## Slide 8: $sp, $fp, $gp
Free Stack
(dynamic data) Stack
Heap (dynamic data)
Data (static data)
Text (Instructions)
dimage
iimage
$gp
high address
low address
incoming args
callee-save space
local variables
outgoing args
$sp
$fp
int foo (int i)
{
return bar (i);
}
int bar (int n)
{
int a = n+1, b = n-1;
return (a*b);
}
stack frame
for foo()
stack frame
for bar()

## Slide 9: Input Format
For each test case, all registers, except PC and $sp, are initialized to 0’s.
iimage.bin
dimage.bin
  More details in Appendix B

## Slide 10: Example code
sum = 0;
for( i = 0; i < 3; i++ ) {
sum += i;
}
andi $t0, $0, 0
andi $t1, $0, 0
loop: slti $t2, $t1, 3
beq $t2, $0, end
add $t0, $t0, $t1
addi $t1, $t1, 1
j loop
end: sw $t0, 0($0)
halt
halt
halt
halt
halt

## Slide 11: iimage.bin
initial value of PC # of words to be loaded into I memory
andi $t0, $0, 0
andi $t1, $0, 0
loop: slti $t2, $t1, 3
beq $t2, $0, end
add $t0, $t0, $t1
addi $t1, $t1, 1
j loop
end: sw $t0, 0($0)
halt
halt
halt
halt
halt
00000000
0000000D
30080000
30090000
292A0003
11400003
01094020
21290001
08000002
AC080000
FFFFFFFF
FFFFFFFF
FFFFFFFF
FFFFFFFF
FFFFFFFF

## Slide 12: dimage.bin
00000400 initial value of $sp
00000003 # of words to be loaded into D memory
12345678 content of D memory begins
9ABCDEF0
13572468

## Slide 14: Output Requirement
snapshot.rpt : contains all register values at each cycle.
error_dump.rpt : contains error messages.
  More details in Appendix C-1 and Appendix D

## Slide 15: Test Case Design
Both iimage.bin and dimage.bin should be placed under a folder named testcase.
The test case should run no more than 500,000 cycles.

## Slide 16: Submission
Create a folder named studentID_01 under /home/archi/studentID
In the folder, please provide the following two folders and corresponding files required:
  simulator : contains your「Makefile」,「README」, and source code files.
    Your Makefile should support the following two functions: make – to build your simulation environment make clean – to erase from the build tree the files built by make all.
  testcase : contains your test case files.

## Slide 17
  Finally, compress the folder studentID_01 as studentID_01.tar.gz, and upload studentID_01.tar.gz and studentID_report.pdf to the iLMS system.
Each project has two due dates. The second due date is one week after the first one.

## Slide 18: Development Environment

## Slide 19: Connect to a Remote Server
Secure Shell (SSH) is a cryptographic network protocol
  secure data communication (sftp)
  remote command-line login
  remote command execution
  other secure network services

## Slide 20
Remote command execution
  OpenSSH
    ssh [user_name]@140.114.75.140
  PieTTY / PuTTY
Secure data communication
  OpenSSH
    sftp [user_name]@140.114.75.140
      ls, cd, get
    scp
      Upload: scp local_file [user_name@140.114.75.140]: remote_directory
      Download: scp [user_name@140.114.75.140]:remote_directory local_file

## Slide 21: scp
scp source destination
I Love 鳥哥之SCP

## Slide 22: sftp
sftp username@140.114.75.140
I Love 鳥哥之 SFTP

## Slide 23: IDE
Editor
  Vim – VI improvement
  Notepad++/ Sublime
Compiler
  GCC: GNU Compiler Collection
Build Automation Utility
  GNU make
Debugger
  GDB: GNU Debugger
Version Control System
  git

## Slide 24: Makefile
Example

## Slide 25: Demonstration

## Slide 26: Related Links
Linux所有資訊都在鳥哥!!!
  http://linux.vbird.org/
Vim (editor)入門圖解
  http://blog.vgod.tw/2009/12/08/vim-cheat-sheet-for-programmers/
GDB (debugging)入門
  http://www.study-area.org/goldencat/debug.htm
版本控制 Git 輕鬆上手
  http://gogojimmy.net/2012/01/17/how-to-use-git-1-git-basic/
  http://backlogtool.com/git-guide/tw/intro/intro2_1.html

## Slide 27: Related Links
Makefile簡易教學
http://goo.gl/nPKhGQ
GCC指令筆記
http://goo.gl/LWX3uk